## Slide 1: UEFI, Open Platforms, and the Defender’s Dilemma
Vincent Zimmer
@vincentzimmer, vincent.zimmer @intel.com | @gmail.com
CanSecWest 2015 Vancouver, Canada

## Slide 2: Agenda
Background on UEFI
Security Features
Trust Model
EDK II on MinnowMax
EDK II on Galileo
Futures
Notes: UEFI, Open Platforms and the Defender's Dillema - Vincent Zimmer, Intel This material will be targeted at end-users and parties building the UEFI Extensible Firmware Interface (UEFI) implementations, especially those based upon the open source edk II. The discussion will be a bottoms-up view on building a hardened UEFI-based platform with open source edk II and full-opened source platform code, such as Intel Quark, as motivating example. The talk will discuss the intent behind the UEFI and PI www.uefi.org specifications, along with the open source infrastructure www.tianocore.org, with a full example in Quark https://downloadcenter.intel.com/Detail_Desc.aspx?DwnldID=23197 and open hardware such as MinnowMax https://uefidk.com/content/minnowboard-max. Topics such as measured boot, signed update, UEFI Secure boot, network boot, and best practices in creating both the underlying firmware at boot and runtime. A historical view of some attacks on BIOS, starting circa 1999, and the wave of UEFI-focused attacks, starting 2006, will also be treated, with an eye toward how the best practices can be used to thwart many of these concerns. Finally, as UEFI is a firmware interface and edk II is software, software cannot solely protect software, so some of the extant and purpose-defined hardware features that help in UEFI defenses will also be reviewed.

## Slide 3: Background on UEFI

## Slide 4: Old Day
Machine
19XX

## Slide 5: Pioneer
8080/Z80
BIOS
(machine specific CP/M)
1974 Basic I/O (Sub) System
by Gary Kildall in CP/M
CP/M

## Slide 6: PC/AT BIOS
8088
BIOS
(de facto standard)
DOS
1981 IBM PC

## Slide 7: PC/AT BIOS -> EFI
IPF (Merced)
EFI
(Intel Standard)
IPF Windows/Linux
2000 Extensible Firmware Interface
Intel/HP IPF

## Slide 8: Broader adoption
IA32/X64/IPF/ARM
UEFI
(Industry Standard)
Windows/Linux
2006 January
Unified Extensible Firmware Interface

## Slide 9: Today
IA32/X64/IPF/ARM
Windows/Linux
UEFI + PI
2006 Aug Platform Initialization
PI
CPU
Module
Generic
UEFI
Drivers
UEFI
Silicon
Module
Platform
DXE
Drivers
• • •
• • •

## Slide 10: Industry Transition
Pre-2000
All Platforms BIOS were proprietary
2000
Intel invented the Extensible Firmware Interface (EFI) and provided sample implementation under free BSD terms
tianocore.org, open source EFI community launched
2004
Unified EFI (UEFI)
Industry forum, with 11 members, was formed to standardize EFI
2005
240 members and growing!
Major MNCs shipping; UEFI platforms crossed most of IA worldwide units; Microsoft* UEFI x64 support in Server 2008, Vista* and Win7*; RedHat* and SuSEl* OS support. Mandatory for Windows 8 client. ARM 32 and 64 bit support. ACPI added.
2015
Notes: Prior to 2000, all platforms BIOS have been using a 20+ years old proprietary, monolithic and assembly language based BIOS architecture
Recognizing the problem and opportunity for platform firmware architecture improvement, Intel invented the Extensible Firmware Interface (EFI) architecture and led the industry to make it a standard….and started to provide sample implementation under free BSD terms in 2000
EFI’s architecture is modular, flexible and extensible…and uses higher programming languages (instead of assembly). EFI helps reduce development cost, improve productivity, reduce TTM and enable platform differentiation
The Open Source EFI community “tianocore.org” was launched in 2004….and a year later, the Unified EFI (UEFI) Industry forum was formed to standardize EFI.
The standard is now called Unified EFI (or UEFI).
Back in 2005, the UEFI forum had 11 members only. Today we have over 160 members representing some of the key industry leaders including all Tier 1 MNCs, Microsoft and BIOS vendors. This significant growth is a healthy indicator of the industry’s acceptance and commitment to the standard.
As you will see in the next few slides, not only did the industry come together to establish a platform firmware standard, but UEFI based products are being developed and deployed….and multiple industry data indicates that by 2010 most systems shipping IA will be using firmware based on UEFI.
The tianocore.org open source community has been instrumental to the success and establishment of new standard “platform” in the pre-boot and firmware space.

## Slide 11: What is UEFI? UEFI Platform Initialization Overview
UEFI 2.4 specifies how firmware boots OS loader
UEFI’s Platform Initialization (PI) 1.3 Architecture specifies how Driver Execution Environment (DXE) Drivers and Pre-EFI Initialization (PEI) Modules (PEIMs) initialize SI and the platform
DXE is preferred UEFI Implementation
PEIMs, UEFI and DXE drivers implement networking, Update, other security features
Hardware
OS
(UEFI or
Today’s)
Pre-boot
Tools
UEFI Specification
Silicon
Component
Modules
Platform
Drivers
UEFI PI Scope - Green “H”
PEI/DXE PI Foundation
Modular components
Network
Hardware
Firmware
OS
Drivers
Libraries
Application
GUI
Human User
Full system stack (user -> hardware)

## Slide 12: Where are we (UEFI firmware)?
SMM / BIOS
CPU
App
OS
App
VM
App
OS
App
VM
VMM / Hypervisor
Memory
Peripherals
Firmware
Hardware
Platform
Privilege
BIOS & OS/VMM share access, but not trust
UEFI + PI SMM
Hypervisor can grant VM direct hardware access
DMA
A specific Peripheral may have its own processor, and its own firmware, which is undetectable by host CPU/OS.
Notes: Specific examples

## Slide 13: What’s in UEFI

## Slide 14
Power on
[ . . Platform initialization . . ]
[ . . . . OS boot . . . . ]
Shutdown
Run Time
(RT)
OS-Present App
Final OS Environment
Final OS Boot Loader
Driver Execution Environment (DXE)
Boot Dev
Select (BDS)
Transient System Load
(TSL)
OS-Absent App
UEFI Shell
Transient OS Boot Loader
Boot Manager
Device, Bus, or Service Driver
UEFI Interfaces Boundary
for PM_AUTH/
EndOfDxe Event
EFI Driver Dispatcher
Architectural Protocols
Pre EFI Initialization (PEI)
CPU Init
Chipset Init
Board Init
TempRam
Security (SEC)
PEI Core
Startup
OEM/PM extensible
3rd party extensible
Overall UEFI Boot Timeline

## Slide 15: UEFI [Compliant] Firmware
SEC
Pre-EFI Init (PEI)
Driver Exec Env (DXE)
Boot Dev Select (BDS)
Runtime / OS
S-CRTM; Init caches/MTRRs; Cache-as-RAM (NEM); Recovery; TPM Init
S-CRTM: Measure DXE/BDS
Early CPU/PCH Init
Memory (DIMMs, DRAM) Init, SMM Init
Continue initialization of platform & devices
Enum FV, dispatch drivers (network, I/O, service..)
Produce Boot and Runtime Services
Boot Manager (Select Boot Device)
EFI Shell/Apps; OS Boot Loader(s)
ExitBootServices. Minimal UEFI services (Variable)
ACPI, UEFI SystemTable, SMBIOS table
CPU Reset

## Slide 16: Specification & Tianocore.org Timeline
UEFI 2.0
PI 1.0
UEFI 2.1
PI 1.1
UEFI 2.3
UEFI 2.2
EDK 1.01: UEFI 2.0
Shell 2.0
PI 1.2
Packaging 1.0
EDK 1.04: UEFI 2.1
PI 1.0
Specifications
Implementation
http://uefi.org
http://tianocore.org SourceForge.net
EDK 1.06: UEFI 2.1+
PI 1.0
SCT
PI 1.0
SCT UEFI 2.0
UDK2010: UEFI 2.3
PI 1.2
All products, dates, and programs are based on current expectations and subject to change without notice.
EDK II*: UEFI 2.1+
PI 1.0
2006 | 2007 | 2008 | 2009 | 2010 | 2011-14
SCT UEFI 2.1
UEFI 2.3.1
UDK2014
UEFI 2.4
PI 1.3
SCT UEFI 2.3
UEFI 2.4
PI 1.3
ACPI5.1
FSP1.0

## Slide 17
USWG
BOD
UNST
USST
……
USRT
USWG
  UEFI Specification Working Group
PIWG
  Platform Initialization Working Group
ASWG
  ACPI Specification Working Group
BOS
  Board Of Directors
USST
  USWG Security Sub-team
  Chaired by Vincent Zimmer (Intel)
  Responsible for all security related material and the team that has added security infrastructure in the UEFI spec
USRT
  UEFI Security Response Team
  Chaired by Dick Wilkins (Phoenix)
  Provide response to security issues.
UNST
  UEFI Network Sub-team (VZ chairs, too)
  Evolve network boot & network security infrastructure for UEFI Specification
Note: Engaged in firmware/boot
Related WG’s of Trusted Computing Group (TCG), IETF, DMTF
www.uefi.org
Working Groups in UEFI
ASWG, PIWG

## Slide 18
UDK2014 Available on Tianocore.org

## Slide 19
Support for UEFI Packages
Import/export modules source/binaries to many build systems
Multiple Development Environments and Tool Chains**
Windows, Linux, OSX
VS2003, VS2005, WinDDK, Intel, GCC
Industry Standards Compliance
UEFI 2.0, UEFI 2.1, UEFI 2.2, UEFI 2.3, UEFI 2.4; PI 1.0, PI 1.1, PI 1.2, PI1.3, ACPI 5.1
Maximize Re-use of Source Code**
Platform Configuration Database (PCD) provides “knobs” for binaries
ECP provides for reuse of EDK1117 (EDK I) modules
Improved modularity, library classes and instances
Optimize for size or speed
Fast and Flexible Build Infrastructure**
4X+ Build Performance Improvement (vs EDKI)
Targeted Module Build Flexibility
Extensible Foundation for Advanced Capabilities
Pre-OS Security
Rich Networking
Manageability
How to build it? UDK2014
** benefit of EDK II codebase
Intel® UEFI Development Kit 2010 (Intel® UDK2010)
Maximize the open source at www.tianocore.org

## Slide 20: Contents
USB 2
USB1.1
PCIe
PCI
ACPI 3
ACPI 2
ACPI 4
UEFI 2.0
UEFI 2.1
UEFI 2.2
UEFI 2.3
UEFI 2.4
PI 1.0
PI 1.1
PI 1.2
Today
EDK I
ECP
New dev
Sustaining
USB 3
ACPI 5.1
Hundreds deep
Since ~2001
Time

## Slide 21: Core evolution
Trunk
1.0
2.0
3.0
4.0
1.1
1.2
1.3
1.4
2.1
2.2
2.3
3.1
3.2
3.3
Time
Different branches to support

## Slide 22: The road from core to platform
Reference Tree
tianocore.org
OEM BIOS
New product
IBV
Existing product
ODM BIOS
New product
Existing ODM product
Commercial product in the field
Consumer product in the field
End users updating?
ODMs updating?
Time
Open Source
Open Source
All
Intel
OEM
IBV
ODM


## Slide 23: Security Features

## Slide 24: Solving Firmware Update
Reliable update story
  Fault tolerant
  Scalable & repeatable
How can UEFI Help?
  Capsule model for binary delivery
  Bus / Device Enumeration
  Managing updates via
    EFI System Resource Table
    Firmware Management Protocol
    Capsule Signing

## Slide 25: Delivering Firmware Binaries
UEFI supports Capsule format
  Tools for capsule generation
  Core logic for capsule handling
Extensible Capsule format
  Self-contained
  Discrete updates
  Composite updates
Firmware Management Protocol allows
  Reading / updating firmware
  Integrity checks

## Slide 26: Rollbacks with fences
Version 1
Version 2
Version 3
Version 1
Version 2
Version 3
Version 4
Version 1
Version 2
Version 3
Version 4
Version 5
Each version fixes some issues with the previous. Since none are known to have security flaws, each new version allows updates to all older versions.
In V4, one of the issues fixed in V3 is realized to be a security fix. V4 will not allow updates to earlier versions, even V3 since it allows update to V2.
Version 5 can now accept only versions 5 and 4.
“Fence”

## Slide 27: Security Solutions
Signed capsule updates
UEFI Secure boot
  local / network
TPM on the platform
  Measured boot
  Root of Trust for Reporting
  Storage
Protect machine configuration & UEFI Secure boot trust anchors
In-band and out-of-band network security

## Slide 28: Guarding & Verifying in Pre-boot
PI & UEFI complement each other to impart platform security through guarding and verification during pre-boot.
PI facilitates platform hardening by guarding internal firmware ingredients that consume reset vector, initialization of CPU, Memory, Chipset etc.
UEFI signing allows robust platform scaling through verified inclusion of external firmware ingredients such as OPROMS into the trust chain

## Slide 29: UEFI Driver Signing
Why? – Origin & Integrity
How? – Authenticode PE
ContentInfo
Certificate
PE file hash
X.509 Certificate
SignInfo
Signed hash of
ContentInfo
PE Header
Attribute
Certificate
Table
Certificate
Directory
Section 1
……
Section N
Type
PE Image
PKCS#7 +
Authenticode Ext

## Slide 30: UEFI Authenticated Variable
Why? – Integrity (no confidentiality)
How? – Time Based
Authenticated Variable
Input Variable Data
Authentication
Certificate
Data Content
Time Stamp
Type
PKCS#7
ContentInfo
Certificate
N/A
X.509 Certificate
SignInfo
Signed hash of
VariableName +
VariableGuid+
Attributes +
TimeStamp +
DataContent

## Slide 31: Put them altogether: UEFI Secure Boot

## Slide 32: UEFI Secure Boot VS TCG Trusted Boot
UEFI authenticate OS loader (pub key and policy)
Check signature of before loading
UEFI Secure boot will stop platform boot if signature not valid (OEM to provide remediation capability)
UEFI will require remediation mechanisms if boot fails
UEFI PI will measure OS loader & UEFI drivers into TPM (1.2 or 2.0) PCR (Platform Configuration Register)
TCG Trusted boot will never fail
Incumbent upon other SW to make security decision using attestation
UEFI Firmware
UEFI OS Ldr, Drivers
Kernel
Drivers
Apps
TPM
record in PCR
UEFI

## Slide 33
Authenticated Variables
PEI FV
DXE FV
Variable
Image Verify
OsLoader.efi
Certificate
+ SignInfo
Certificate
+ SignInfo
PK
KEK
1. Enroll
2A. Signed Image Discover
2B. Signature Verification
2C. Signed Image Load & Measure to
TPM
db
Certificate
dbx
Certificate
OpRom.efi
3. Post ship update DB
UEFI Secure Boot Ceremony-
Ellison, Carl M. “Ceremony Design and Analysis,” IACR Cryptology ePrint Archive (2007): 399. https://eprint.iacr.org/2007/399.pdf

## Slide 34: Relevant open source software packages/routines for Authorization flow
See Rosenbaum, Zimmer, "A Tour Beyond BIOS into UEFI Secure Boot,“ for more details
Notes: 1 Authenticate the image’s format and structure.
2 If the image is unsigned: If its signature in in the authorized database (DB) and is not in the forbidden database (DBX), run the image, otherwise deny.
3 If the image is signed, check if its certificate has been authorized (i.e. the image’s certificate is found in the KEK or the authorized database (DB), and is not in the forbidden database (DBX)).
If the image’s certificate is authorized, then unless the image’s signature is in the forbidden database (DBX), run the image
4 If the image’s certificate has not been authorized, then check its signature. If its signature is in the authorized database (DB) and is not in the forbidden database (DBX), run the image, otherwise deny running the image
Signature – is the SHA256 hash of the PE/COFF image.
Certificate – is the image’s Authenticode certificate containing the public key used to sign the image.
Certificate Authorized
  In UDK2010.SR1.UP1 and earlier implementations, an image’s certificate is authorized if it matches or chains to a KEK or DB entry, (or both).
  However, the UEFI 231C specification now states on page 227 that an certificate in DB can match or chain to certificates in KEK, or PK.
Since certificates in KEK must chain to certificates in PK, this clarification implies that a certificate in DB is authorized if it chains to a certificate in PK.
I.e. during SetVariable, KEK is used to authorize DB (and DBX) variable entries and PK is used to authorized KEK entries. However KEK is not used to authorize an image to be run during LoadImage.
Implementations complying with this updated interpretation authorize an image’s certificate if it matches or chains to only a DB entry.

## Slide 35
Load the UEFI image as long as it is trusted
Linux Update – Multiple OS Boot with MOK

## Slide 36
Either the UEFI CA key or SUSE key will let the shim boot with UEFI secure boot
Multi-Signature Support for Shim

## Slide 37
  RandomNumberGenerator
  UEFI driver implementing the EFI_RNG_PROTOCOL from the UEFI2.4 specification
  TCG
  PEI Modules & DXE drivers implementing Trusted Computing Group measured boot
  EFI_TCG_PROTOCOL and EFI_TREE_PROTOCOL from the TCG and Microsoft MSDN websites, respectively
  UserIdentification
  DXE drivers that support multi-factor user authentication
  Chapter 31 of the UEFI 2.4 specification
  Library
  DxeVerificationLib for “UEFI Secure Boot”, chapter 27.2 of the UEFI 2.4 specification + other support libs
  VariableAuthenticated
  SMM and runtime DXE authenticated variable driver, chapter 7 of the UEFI2.4 specification
  https://svn.code.sf.net/p/edk2/code/trunk/edk2/SecurityPkg
UDK2014 SecurityPkg

## Slide 38
  Variable Lock Protocol
  Make variables read-only https://github.com/tianocore/edk2/blob/master/MdeModulePkg/Include/Protocol/VariableLock.h
  Lock Box
  Protect content across re-starts
  https://github.com/tianocore/edk2-MdeModulePkg/blob/master/Include/Protocol/LockBox.h
  Capsule Update
  Generic capsule update driver support
  http://comments.gmane.org/gmane.comp.bios.tianocore.devel/8402
  https://svn.code.sf.net/p/edk2/code/trunk/edk2/
Additional capabilities in the open source

## Slide 39
Analyze and Mark external Interfaces where input can be attacker controlled data, comment headers
  /**
  Install child handles if the Handle supports GPT partition structure.
  Caution: This function may receive untrusted input.
  The GPT partition table is external input, so this routine
  will do basic validation for GPT partition table before install
  child handle for each GPT partition.
  @param[in] This Calling context.
  @param[in] Handle Parent Handle.
  @param[in] DevicePath Parent Device Path.
  **/
  EFI_STATUS
  PartitionInstallGptChildHandl
UDK2010 example: http://edk2.svn.sourceforge.net/svnroot/edk2/trunk/edk2/MdeModulePkg/Universal/Disk/PartitionDxe/Gpt.c
Code Management

## Slide 40
CPU/SOC
(Intel)
Intel Boot Guard
Start Block PEI
(OEM)
Executable
Policy
Policy Engine
Enforces
BIOS DXE/UEFI
(OEM)
Executable
OS Loader/Kernel
(OSV)
Executable
Policy
Policy Engine
Enforces
Policy
Policy Engine
Enforces
OEM PI Verification
Using PI Signed
Firmware Volumes Vol 3, section 3.2.1.1
of PI 1.3 Specification
OEM UEFI 2.4 Secure Boot
Chapter 27.2 of
The UEFI 2.4 Specification
Intel® Device Protection Technology with Boot Guard
http://www.intel.com/content/dam/www/public/us/en/documents/product-briefs/4th-gen-core-family-mobile-brief.pdf
Intel® Boot Guard

## Slide 41: Technologies – putting it together
Reset
Erase flash part
Overwrite flash part
Erase op ROM
Overwrite op ROM
Network attacks
Spoof boot loader
Different colors for different vendors
System BIOS
NIST SP800-147. PEI recovery. DXE SMM, UEFI Core
Option ROMs
BIOS device drivers
Network Boot
IPv6 for the cloud
OS Boot loader
BIOS loads the OS To BIOS, VM is an OS
SP800 -147
UEFI 2.4
Threats
Assets
ROM Swap
Bit rot
BIOS Flash
H/W
Spec
TCG Measurements into PCRs 0..7

## Slide 42: Trust Model

## Slide 43: System
Data | CP/M (1974) | IBM PC (1981) | PC (1999) | PC (2012)
BIOS ROM | <4K | 40K | 512K | 4M
Processor | 8080 | 8088 | Pentium III | Ivy Bridge
OS | CP/M | DOS | Win98 | Win8

## Slide 44: Security
Data | CP/M (1974) | IBM PC (1981) | PC (1999) | PC (2012)
Malware | [1949]: John von Neumann - Theory of self-reproducing automata [1971]: Bob Tomas: Creeper - “I’m Creeper: Catch me If you Can” | [1984]: Fred Cohen- Computer Viruses - Theory and Experiments (VAX, UNIVAC) [1986]: Farooq Alvi – Brian (IBM PC) | [1999]: CIH (Intel 430TX) | [2011]: BMW /Mebromi (Award BIOS) *[2005~] BootKit *[2006~] BiosRootkit *[2006~] SMM *[2008] Password *[2008~] NIC *[2009] BMP *[2009] ME *[2009~] KBC/EC *[2011] Battery Bootkit S3 SMM
Security | [1972] Anderson - Computer Security Technology Planning [1973] Bell-LaPadula [1977] Biba Integrity [1989] Clark Wilson | Bios Password | Flash Protection [1992] SMM in i486SL | [2003] TCG [2006] TXT [2006] UEFI Secure Boot [2009] SMRR [2014] Intel ® Boot and BIOS Guard

## Slide 45: Security Challenges
Different elements in platform from many vendors
How to establish trust anchor in the hardware
How to protect elements
How to protect the platform
How to allow platform scaling

## Slide 46
BIOS
BIOS Potential Attack Surfaces
Unsafe
Coding
Practices
Server
Mgmnt
Interfaces
Shell
Apps &
Diags
BIOS
Update
Interfaces
Option
ROMs
Standard
APIs
System
Mgmnt
Mode
BIOS
Vendor
Hooks
Notes: (Pitfall)
Field Updatable
  BIOS, like other firmware, often needs to be updated in the field post-deployment.
Standard APIs
  BIOS unlike many other custom firmware implementations is more and more being developed using standard UEFI interfaces.
  These are published (hint, hint)
Intimate Platform control Points
  Subverting BIOS opens up direct and deep handles on a platform which can be exploited without knowledge of higher-level software (SMM).
Option ROMs
  Plug in that PCIe card and invite its Option ROM to the party.
    OROM code pulled in by BIOS at boot time

## Slide 47
Pre-Boot Threats
Bootkits
BIOS Malware
Device FW Malware
HVM Rootkits (Blue Pill)
SMM Rootkits
ACPI Rootkits
Evil Maid
Option ROM Malware
UEFI Rootkits
HW Trojans

## Slide 48
Missed a Detail
Source: Jeff Forristal

## Slide 49
Security Fundamentals

## Slide 50
Security Fundamentals

## Slide 51: What Could Possibly Go Wrong???
SMM IPL
Power on
Security
(SEC)
[ . . Platform initialization . . ]
Pre EFI
Initialization (PEI)
Driver Execution Environment (DXE)
Boot Dev
Select (BDS)
[ . . . . OS boot . . . . ]
Transient System Load
(TSL)
Shutdown
After Life
(AL)
Run Time
(RT)
?
OS-Present App
Final OS Environment
Final OS Boot Loader
OS Absent Application
Transient OS Boot Loader
Boot Manager
CPU Init
Chipset Init
Board Init
verify
Device, Bus, or Service Driver
Exposed
Platform Interface
Pre Verifier
EFI Driver Dispatcher
Boot Services Runtime Services
security
SMM Handler
SMM Intrinsic Services
UEFI Runtime, ACPI, SMBIOS,….

## Slide 52: Things need consider
Protect
Detect
Recover
System
Firmware

## Slide 53: What to build & defend – Rationale for a threat model
“My house is secure” is almost meaningless
  Against a burglar? Against a meteor strike? A thermonuclear device?
“My system is secure” is almost meaningless
  Against what? To what extent?
Threat modeling is a process to define the goals and constraints of a (software) security solution
  Translate user requirements to security requirements
We used threat modeling for our UEFI / PI codebase
  We believe the process and findings are applicable to driver implementations as well as UEFI implementations in general

## Slide 54: Defining, using a threat model
A Threat Model (TM) defines the security assertions and constraints for a product
  Assets: What we’re protecting
  Threats: What we’re protecting it against
  Mitigations: How we’re protecting our Assets
Use TM to narrow subsequent mitigation efforts
  Don’t secure review, fuzz test all interfaces
  Select the ones that are critical
TM is part science, part art, part experience, part nuance, part preference
  Few big assets vs lots of focused assets

## Slide 55: We don’t always get to choose our Assets
PE/COFF
Operating System
Option ROM
SMM
This reg That reg Other bit
NIST
Security “Researchers”
UEFI, TCG, OSV
Internal Research
Source
BIOS Flash
Build tools
SMM
Boot flow
S3  S0
Internal Research

## Slide 56: Flash**
NIST SP800-147 says
  Lock code flash except for update before Exit Mfg Auth
  Signed update (>= RSA2048, SHA256)
  High quality signing servers
  Without back doors (“non-bypassability”)
Threats
  PDOS – Permanent Denial of Service
    System into inefficient room heater
  Elevation of privilege
    Owning the system at boot is an advantage to a virus
Known attacks
  CIH / Chernobyl 1999-2000
  Mebroni 2010
Mitigations include
  Reexamining flash protection methods – use the best even if its new
  Using advanced techniques to locate and remove (un)intentional backdoors
** or tomorrow’s equivalent NV storage

## Slide 57: SMM
SMM is valuable because
  It’s invisible to Anti Virus, etc
  SMM sees all of system RAM
  Not too different from PCI adapter device firmware
Threats
  Elevation
    View secrets or own the system by subverting RAM
Known attacks
  See e.g Duflot, Legbacore
Mitigations include
  Validate “external” / “untrusted” input
  Remove calls from inside SMM to outside SMM
SMM

## Slide 58: Resume from S3
ACPI says that we return the system to the S5S0 configuration at S3S0
  Must protect the data structures we record the cold boot config in
Threats
  Changing data structures could cause security settings to be incorrectly configured leaving S3
  Reopen the other assets’ mitigated threats
Known attacks
Mitigations include
  Store data in SMM -or-
  Store hash of data structures and refuse to resume if the hashes don’t compare
This reg That reg Other bit

## Slide 59: Tool chain
Tools create the resulting firmware
  Rely on third party tools and home grown tools
  Incorrect or attacked tools leave vulnerabilities
Threats
  Disabled signing, for example
Known attacks
  See e.g. Reflections on Trust, Ken Thompson**
Mitigation
  Difficult: For most tools, provided as source code
  Review for correct implementation
  Use static, dynamic code analysis tools
    PyLint for Python, for example
** CACM, Vol 27, No 8, Aug, 1984, pp. 761-763

## Slide 60: Boot flow
Secure boot
  Authenticated variables
  Based on the fundamental Crypto being correct
  Correct location for config data
Threats
  Run unauthorized op roms, boot loaders
  PDOS systems with bad config variables
Known attacks
Mitigations include
  Sanity check config vars before use, use defaults
  Reviews, fuzz checking, third party reviews, etc.
PE/ COFF

## Slide 61: TM to Modules: Boot flow
Buff o’flow to pwn sys. Sanity check config pkts.
Classic net attacks Fuzz test packets
USB Dev
ATAPI Dev
SCSI Dev
LAN NIC
USB Stack
ATAPI Stack
SCSI Stack
LAN Stack
File System
PE/Coff Loader
Crypto
Auth Var Svcs
Authenticated Variables
boot control variables
Setup Variables
Var Svcs

## Slide 62: Assets or not?
Variable content sanity checking?
  If you randomly fill in your Setup variables, will your system still boot?
  Fit in as a part of boot flow
ACPI? We create it but don’t protect it
TPM support? We fill in the PCRs but don’t use them (today)
Quality ≠ Security
?

## Slide 63
Vulnerability Cases:
  Unauthorized Firmware Update
  Unauthorized 3rd Party Code
  Critical Register Unlocked
  Buffer Overflow
  Secret Used but not Cleared
  Default Passphrase to Access
Vulnerability VS Threat
Threat:
  S: Spoof user identity
  T: Tampering
  R: Repudiation
  I: Information disclosure
  P: Permanent Denial of Service
  E: Elevation of privilege
  D: Denial of service

## Slide 64: EDK II on MinnowMax

## Slide 65: MinnowMax
Open hardware platform
Baytrail single or dual core
From http://firmware.intel.com/projects
This project focus in on the firmware source code (and binary modules) requried to create the boot firmware image for the MinnowBoard MAX. The UEFI Open Source (EDKII project) packages for MinnowBoard MAX are available at http://tianocore.sourceforge.net/wiki/EDK2. To learn more about getting involved in the UEFI EDKII project visit the How to Contribute page.
The source code builds using Microsoft Visual Studios and GNU C Compiler (for both 32 and 64 bit images) - production and debug execution environments. The source code builds the same UEFI firmware image shipping on MinnowBoard MAX.
- See more at: http://firmware.intel.com/projects#sthash.1oOc8srY.dpuf

## Slide 66: Intel® Firmware Support Package (FSP) Overview
The Intel ® FSP provides processor & chipset initialization in a format that can easily be incorporated into many existing boot loader frameworks without exposing the Intellectual Property (IP) of Intel.
  Distributed as single binary
  Silicon PEIMs packaged into FSP
  Plugs into existing f/w frameworks
  Binary customization
More information at www.intel.com/fsp

## Slide 67: Intel® FSP Boot Flow
NotifyPhase
Reset
Vector
Switch to 32-bit Mode
Load Microcode
Temp Ram Init
Mem Init
Companion Chip Init
Processor Init
Find FSP Entry Point
Parse Return Data
Platform Init
Bus and Device Init
Boot Device Init
NotifyPhase
Intel® FSP
App
Jump to FSPinit
NotifyPhase Code
Load OS or other payload
PostPciEnum
ReadyToBoot
Boot Loader
FSP
Notes: Boot loader owns reset vector
      Bootloader contains the real mode reset vector handler code
      Bootloader calls TempMemInit to create stack
      Bootloader calls FspInit to initialize memory and chipset
      Bootloader calls NotifyPhase at proper stages

## Slide 68: MinnowMax
Focused on the maker community, but….
64-bit Intel® AtomTM E38xx Series SOC
Has UEFI Secure Boot
Built off of live tree
Ability to update w/ latest capabilities on http://www.tianocore.org

## Slide 69: EDK II on Galileo

## Slide 70: Intel® Quark™ SoC – Hardware Overview
32 bit Intel® Pentium® ISA-class processor
PCI
USB
I2C
Single core

## Slide 71: UEFI for Intel® Quark™ SoC
First fully open source Intel-based platform
Builds on Intel® UDK2014 packages like MdePkg, MdeModulePkg w/ a 32-bit build, adding
  IA32FamilyCpuBasePkg
  QuarkPlatformPkg
  QuarkSocPkg
Standard build is 1 Mbyte image w/full features
  Capsule update, SMM, S3, PCI, recovery, full UEFI OS support, FAT OS support, UEFI variables
Notes: Split into 2
Directory listing of packages used for quark/galileo

## Slide 72: Quark and security
Support for I2C-attached TPM
Hardware Secure Boot option
UEFI Secure Boot implementation
UEFI Capsule update support w/ hardware verification assist
…..
Demonstrates one way to build out UEFI Security Features w/ a full open source platform tree

## Slide 73: Futures

## Slide 74: Integrity analysis of Pre-OS via Compartments – CW/BIBA
Business goals dictate isolation boundaries called compartments (cpts)
  Platform Manufacturer wants to protect self from 3rd party pre-OS and OS/Hv
  OS/Hv- protect self from pre-boot extensibility
  Idealized isolation boundary is a compartment (cpt)–
    Not a thing like process, interface table, handle etc
  Security types are actual data types that are used in the cpt.
    Eg: Smm_code_t, efi_iface_tbl_data_t in OEM cpt
Security analysis checks if something is a compartment
  Checking a number of information flow rules
    Code and data in compartment have verifiable integrity
      Compartment needs storage isolated from other compartments
      Compartment needs execution isolation
    Compartment transitions have chokepoints and are protected via guards
      Interfaces into the compartment for code and data must be validated
    Admin model of compartment must be fully specified
      Admin tasks must be “minimized” to reduce TCO & chance of bugs
    Audit (e.g.,TPM measurements)– All integrity affecting operations must be audited
      Availability of audit log is also a requirement

## Slide 75
Notes: Define isolation compartments to satisfy the goals
Analyze compartment isolation
  Protection of code and data throughout compartment lifecycle
  Protection of interfaces exposed by compartment
  Compartment admin and policy data protection
    Minimize admin tasks and code
  Per-compartment audit (eg: using TPM)
Analysis mechanism
  Define security types and roles for each compartment based on EFI architecture
  Perform an information flow analysis to look for unguarded write flows from lower integrity compartments to higher integrity compartments
  See XLS spreadsheet for full listing of compartment types
75

## Slide 76
Notes: Define isolation compartments to satisfy the goals
Analyze compartment isolation
  Protection of code and data throughout compartment lifecycle
  Protection of interfaces exposed by compartment
  Compartment admin and policy data protection
    Minimize admin tasks and code
  Per-compartment audit (eg: using TPM)
Analysis mechanism
  Define security types and roles for each compartment based on EFI architecture
  Perform an information flow analysis to look for unguarded write flows from lower integrity compartments to higher integrity compartments
  See XLS spreadsheet for full listing of compartment types
76

## Slide 77
Notes: Define isolation compartments to satisfy the goals
Analyze compartment isolation
  Protection of code and data throughout compartment lifecycle
  Protection of interfaces exposed by compartment
  Compartment admin and policy data protection
    Minimize admin tasks and code
  Per-compartment audit (eg: using TPM)
Analysis mechanism
  Define security types and roles for each compartment based on EFI architecture
  Perform an information flow analysis to look for unguarded write flows from lower integrity compartments to higher integrity compartments
  See XLS spreadsheet for full listing of compartment types
77

## Slide 78: Moving Forward
More open source examples
Test tools complement the SCT, but the community can do more!
Continue to evolve development philosophy
“Testing shows the presence, not the absence of bugs” (Dijkstra,1970)
Better Living Through Tools? (Zimmer, 2013)
Getting code coverage closer to 100%?
Early effort using DDT with EDK II, Moving to KLEE (open source)
More fuzzers, from custom to public (e.g., Peach)
More Isolation – lots of hardware, esp. that built for OS/Hv. Leverage for platform firmware where it makes sense
Map the CW/BIBA CPT analysis to specs & code
Information flow and analysis
NX, ALSR, Stack Canaries

## Slide 79: References
UEFI Forum http://www.uefi.org
EFI Developer Kit II http://www.tianocore.org
White papers, training, projects http://firmware.intel.com
CHIPSEC: https://github.com/chipsec/chipsec
Trianocore security advisories
UEFI Forum USRT (security@uefi.org , PGP key)
Intel PSIRT (secure@intel.com, PGP key)
Books http://www.apress.com/apressopen UEFI SHELL
UEFI Overview UEFI Intel Technology Journal
Quark Soc X1000 Version 1.1.0 BIOS https://downloadcenter.intel.com/download/23197/Intel-Quark-BSP
MinnowMax http://www.minnowboard.org/meet-minnowboard-max/

## Slide 80: Thank You CanSecWest 2015